# Morse Code Program Notes
## Spacing rules
- dot – one unit
- dash – three units
- within character – one unit
- between characters – three units
- between words – seven units
## Speed Calculations
- A ‘standard’ word has 50 dots
- 1 WPM – dot length = 1200ms
- 5 WPM – dot length = 240ms
- 8 WPM – dot length = 150ms
- 10 WPM – dot length = 120ms
- 12 WPM – dot length = 100ms
- 15 WPM – dot length = 80ms
- 20 WPM – dot length = 60ms
- 25 WPM – dot length = 48ms

## The Code
#### Alphabet
A: ● ▬	B: ▬ ● ● ●	C: ▬ ● ▬ ●	D: ▬ ● ●	E: ●
F: ● ● ▬ ●	G: ▬ ▬ ●	H: ● ● ● ●	I: ● ●	J: ● ▬ ▬ ▬
K: ▬ ● ▬	L: ● ▬ ● ●	M: ▬ ▬	N: ▬ ●	O: ▬ ▬ ▬
P: ● ▬ ▬ ●	Q: ▬ ▬ ● ▬	R: ● ▬ ●	S: ● ● ●	T: ▬
U: ● ● ▬	V: ● ● ● ▬	W: ● ▬ ▬	X: ▬ ● ● ▬	Y: ▬ ● ▬ ▬
Z: ▬ ▬ ● ●

#### Numbers
0: ▬ ▬ ▬ ▬ ▬	1: ● ▬ ▬ ▬ ▬	2: ● ● ▬ ▬ ▬	3: ● ● ● ▬ ▬	4: ● ● ● ● ▬
5: ● ● ● ● ●	6: ▬ ● ● ● ●	7: ▬ ▬ ● ● ●	8: ▬ ▬ ▬ ● ●	9: ▬ ▬ ▬ ▬ ●
#### Punctuation
. - ● ▬ ● ▬ ● ▬	, - ▬ ▬ ● ● ▬ ▬	? - ● ● ▬ ▬ ● ●	‘ - ● ▬ ▬ ▬ ▬ ●	/ - ▬ ● ● ▬ ●
( - ▬ ● ▬ ▬ ●	) - ▬ ● ▬ ▬ ● ▬	: - ▬ ▬ ● ● ●	= - ▬ ● ● ● ▬	+ - ● ▬ ● ▬ ●
- - ▬ ● ● ● ● ▬	“ - ● ▬ ● ● ▬ ●	@ - ● ▬ ▬ ● ▬ ●	! - ▬ ● ▬ ● ▬ ▬	& - ● ▬ ● ● ●
; - ▬ ● ▬ ● ▬ ●	_ - ● ● ▬ ▬ ● ▬

## Program Considerations
#### Presenting Character Groups or Lines
- Set WPM
- Set clock to dot length
- encode spacing as on/off clock cycles.
#### Listening for Code
- Get speed sample from user.
- calculate dot_length in ms.
- set clock to 10 units / dot_length.
- dot / space = 8 - 14 clock cycles.
- dash / letter space = 20 – 40 clock cycles.
- word space = 50 – 90 clock cycles.
- start tone_counter on start of tone.
  stop mute_counter and test the length. Figure out char, letter, word.
  Reset mute_cnt.
- Stop tone_counter on end of tone.
  Start mute_counter.
  Test tone length. Figure out dot or dash.
  Reset tone_cnt.